## Slide 1
Source: V. Duflot, OPAR
alexey.tikhomirov@dal.ca
Lidar Working Group
2018 Report
Thierry Leblanc
Wolfgang Steinbrecht

## Slide 2
NH:
Eureka O3/Temp
Thule Temp
Hohenpeissenberg O3/Temp
Payerne Temp/H2O
OHP O3
OHP Temp/Aer/H2O
OHP tropo. O3
Huntsville Tropo. O3
TMF O3/Temp/Aer
TMF Tropo. O3
TMF H2O
MLO O3/Temp/Aer (JPL)
MLO Aer (NOAA)
12-month summary (1): operational and funded(?), reasonably resolved issues
SH:
Reunion-Maïdo O3
Reunion-Maïdo Tropo. O3
Reunion-Maïdo Temp/Aer
Reunion-Maïdo H2O
Lauder O3 (Temp?)
DDU Aer
Dome C Aer
Mobile:
GSFC TROPOZ Mobile Tropo. O3
GSFC STROZ Mobile O3/T/Aer/H2O
GSFC AT Mobile T/Aer/H2O
12 out of 19 (63%)
are NDACC compliant
measured & submitted data since 09/2017

## Slide 3
12-month summary (2): chronic issues, with hope
London Ont. Temp
instrumental problems, no data archiving, but instrument working again
Garmisch/Zugspitze Aer
unclear instrument, chronic lack of processing, data archiving, but new PI
Potenza, H2O/Temp/AER
no routine operation? Submitted 1 month of data
Rome Tor-Vergata, H2O/Temp
technical issues, low budget, short staffed, but submitted data 2003 to 2010
recent measurements EARLINET

## Slide 4
12-month summary (3): chronic issues, little hope
Andoya
Laser failure. Replacement planned for several years (no support)
Boulder Aer
Instrument failure, no staffing, re-open 2019?
Rio Gallegos O3/T/Aer
Gas supply, instrument, communication failure
ALVICE Mobile H2O
No funding for NDACC, transferred from GSFC to Howard U./Beltsville
Sondrestromfjord Temp
!! station closed !!

## Slide 5
12-month summary (4): The water vapor case…
All H2O Lidars:
almost no data archived despite data format finalization in late 2016
However:
Format update in October 2017: Efforts to push for data archiving ongoing
1 hdf-File by Table Mountain
1 month AMES by Potenza
2003 to 2010 AMES by Rome Tor-Vergata

## Slide 6
LAVANDE (phase 2) at OHP, March 2018:
GSFC-STROZ (McGee), LATMOS O3 (Godin-Beekmann), T (Keckhut)
Hohenpeissenberg, October 2018:
GSFC-STROZ (McGee), DWD O3 and T (Steinbrecht)
12-month summary (5)
Past and future campaigns
future plans:
LAVANDE (phase 1) at OHP, July 2017:
GSFC-STROZ (McGee), LATMOS O3 (Godin-Beekmann), T (Keckhut)
Maïdo-Reunion MORGANE-2 (some time in 2019/2020):
GSFC-STROZ (McGee), OPAR O3 (Portafaix), T (Keckhut), H2O (Duflot)
Lauder (2020?):
GSFC-STROZ (McGee), NIWA O3 (and T) (Querel)
Rio Gallegos (20xx):
GSFC-STROZ (McGee), CEILAP O3 and T (Quel, Salvador, Wolfram)

## Slide 7
NDACC Lidar Working Group Website
Host Change
Former site managed by RIVM (Netherlands): (hosted by private company)
http://ndacc-lidar.org/
To be discontinued December 2018
New site hosted by JPL-Table Mountain:
https://tmf-lidar.jpl.nasa.gov/NDACC_LWG
Currently under construction (almost finished) To be public Oct-Nov 2018 (after JPL Public release approval)

## Slide 8
Lidar Working Group Meetings
TOLNET + LWG Meeting: 2018
Where: Huntsville, Alabama
When: May 2018
LWG Meeting: 2016
Where: Payerne, Switzerland
When: Summer 2016

## Slide 9
Common Interests
JPL
ESRL
UAH
GSFC
LaRC
ARC
ECCC
Current Common interests
Satellite validation
Theory and Analysis
Instrument Accuracy Assessment
Instrumental and data processing issues
Consider these Potential Common Interests
STE
Tropospheric Structure and Evolution
PBL
Air Quality observations -- 24/7 with coming geostationary satellites
Mobile Systems
5th Annual TOLNet Meeting 7-8 May 2017, Huntsville, AL USA
1st Joint TOLNet & NDACC Meeting 8-9 May 2017, Huntsville, AL USA
TOLNET & NDACC (lidars)

## Slide 10
SG Issues from Station Reports

## Slide 11
need for agency support for water vapor intercomparison campaign (MOHAVE) at Table Mountain in 2019
U.S. Army proposal to deploy new telecommunication devices at Mauna Loa that could impair the quality of future measurements (cf. MLO / Leblanc station report)
automatic processing of tropospheric ozone lidar data (cf. OHP / Ancellet station report)
tropospheric temperature by rotational Raman lidar for NDACC (cf. Payerne / Haefele station report)
OEM retrievals for Rayleigh temperature, water vapor, ozone … (cf. London, Ontario / Bob Sica)
Eureka data analysis, data archiving (cf. Tikhomirov / Drummond station report)
SG issues from station reports (1)

## Slide 12
Practical support in processing and archiving the data. (Rome Tor-Vergata / Liberti)
Actions to make the data more visible and used (participation to conferences, publications). (Rome Tor-Vergata / Liberti)
Fundings. (Rome Tor-Vergata / Liberti)
SG issues from station reports (2)
NDACC / LWG Chairs can help
but we are not baby-sitters (processing, submission)
nor magicians (funding, publications, conferences)

## Slide 13
Science Highlights

## Slide 14
Rayleigh lidar temperature climatology (1994 – 2013)
Optimal estimation for lidar
From B. Sica, A. Jalali
classical Hauchecorne & Chanin
Optimal Estimation
Notes: Make bigger

## Slide 15
TMF O3
Lauder O3
New GLASS Data Processing examples
Eureka O3
From T. Leblanc

## Slide 16
Water vapor validation
From V. Duflot
MORGANE Campaign
GRUAN CFH – Reunion Raman Lidar
40 min
profiles

## Slide 17
Tropospheric Water Vapour 2009 - 2017
Since 2008 RALMO has produced on average 1 profile every hour, i.e. 50% availability of tropospheric profiles.
Payerne Raman Lidar
From G. Martucci

## Slide 18
~ 4-5 ppmv
October 2016
Water vapor above TMF
From T. Leblanc

## Slide 19
10-40 ppmv !!!!
October 2017
Water vapor above TMF
From T. Leblanc
Jens Reichardt
Lindenberg
27 August 2018
Fluorescence from
Canadian wildfire aerosol

## Slide 20
Stratospheric Aerosol @ OHP
From S. Khaykin

## Slide 21
Stratospheric Aerosol
From J. Barnes

## Slide 22
Polar Stratospheric Clouds
From M. Snels
Blue = ice, Green = NAT mixtures
Red = enhanced Nat mix, Orange= STS
PSC type | McMurdo gb [%] | McMurdo CALIOP [%]
STS | 25.3 | 24.1
NAT mixtures | 58.4 | 54.9
Enhanced NAT Mix | 2.9 | 5.6
Ice | 13.4 | 15.3
Relative abundances PSC types
Vertical distribution 2006-2010
CALIOP vs groundbased
McMurdo (2006-2010)

## Slide 23
SAGE III / ISS Validation @ OHP
From S. Godin-Beekmann

## Slide 24
LAVANDE, Jul. 2017, Mar. 2018 @ OHP

## Slide 25
NDACC ozone time series
From W. Steinbrecht
AI PO-11
Also: SPARC LOTUS
Ozone trends report

## Slide 26
SCOOP Take Home Message: It’s just the beginning for TOLNet…
1. SCOOP results showed that AMOLITE, LMOL, TMT, TOPAZ and TROPOZ can be considered “validated”
0 20 40 60 80 100 125 150 175
O3 ppbv
SCOOP
Is that the signature of the Blue Cut Fire?
2. Any instrumental change or data processing change should, in theory, be followed by re-validation
3. Automated systems like AMOLITE would surely add value to TOLNet
Any volunteer to start a new, post-SCOOP study?
31-day continuous measurements by AMOLITE

## Slide 27
Tropospheric ozone in Huntsville
From S. Kuang
UTC = local + 6
high ozone above highway
less ozone during solar eclipse
ozone titrated away at night

## Slide 28
Thule
can we see clearer now?
Source: T. DiIorio, ENEA

## Slide 29: where do we stand ?
what can we do
  not much?
  (semi-)automatic operation
  share methods & code, simplify, use batch files & better software
  train people, keep positions
competition
  satellites, sondes, GRUAN
  EARLINET, ACTRIS
  sondes, satellites(?), FTIR, µWave
  sondes, GRUAN
NDACC lidar difficulties
  lasers (and funding)
  long nights
  processing & data submission
  aging & retirements
NDACC lidars
  unique for strato+meso temperature
  unique for aerosol
  good for strato + tropo ozone
  water vapor

## Slide 30: successes
part of SPARC-LOTUS ozone profile trend activity
part of 2018 WMO/UNEP ozone assessment
Lauder lidar looking good again
Reunion / Maido established & looking good
Dome-C transition worked
ISSI Team uncertainty standardization
OHP intercomparison + more planned
challenges
Andoya, Rio Gallegos, Eureka, Sondre Stromfjord, Tor Vergata, …
slow submission, hdf still not widespread, hdf-aerosol missing
aging & retirement
perception of „same old“
Khaykin et al. aerosol time series